## Slide 1: Pre-Lab Presentation: Fluid Flow in a Straight Pipe
ENGR30002 Semester 2, 2020
Group 34
Declan Falls (1083946)
Michael Wu (1079924 )
Maria Vianney Gracia (958867)

## Slide 2: Schematic Diagram
Apparatus Set-Up

## Slide 3: Schematic Diagram

## Slide 4: Experimental Procedure
Step-by-step Instructions

## Slide 5: Experimental Procedure
Set apparatus following the schematic diagram.
Check that gauges and flow meters are mounted safely and in the correct position.
Ensure all valves are set to close. All flow meters and pressure gauges should read 0 before there is any flow through the pipe.
Ensure tubes and gauges are free of dirt or moisture.
Record pipe diameter and distance between pressure gauge connections.
Open valve for the rotameter and set the flowrate to 6L/hr.
Check for leakage.

## Slide 6: Experimental Procedure
Open valve for the wet-wet digital pressure gauge. If pressure drop reading is sufficiently low, open valves for the other two pressure gauges.
Wait until pressure readings in the gauges stabilise then take measurements.
After a measurement of the pressure drop across the pipe is taken, change the flow rate to the next desired value.
Repeat step 9 after an equilibration period.
Should at any point the pressure drop go above the range of a pressure gauge, close the valves connecting the line to that pressure gauge.

## Slide 7: Experimental Procedure
This will result in 7-10 readings in each flow regime: laminar, transition, and turbulent.
After completion of all trials with the different flow rates, turn off the water supply.
Close the rotameter valve.
Close the pressure gauge valves.
Disconnect lines from inlet and outlet of pipe.

## Slide 8: Calculation Steps
Fanning friction factor and Reynolds Number

## Slide 9: Measured Parameters
Independent variable
Dependent variable
Controlled variable

## Slide 10
From the volumetric flow rate (Q) we can find the flow velocity (V) as
          Q = V x A
After rearrange
          V= Q/A

## Slide 11
Using the Mechanical Energy Balance

## Slide 12
This leaves,
which can be rearranged to
Since the only unknown variable in this equation is , we can solve this equation using all the values of the known variables.

## Slide 13: Finding Reynolds Number
where is the viscosity of water.
is the density of water.
is the diameter of the cross-sectional area of the pipe.
is the velocity of the fluid.

## Slide 14: Justifications
Choices Made in Experimental Procedures

## Slide 15
Number of Runs
Laminar flow: Re < 2000
Transition flow: 2000 < Re < 3000
Turbulent flow: Re > 3000
Notes: For our experiment We want to get equal amount of data points in the three flow regime: laminar, transition, and turbulent.
Laminar flow: Re < 2000.
Transition flow: 2000 < Re < 3000.
Turbulent flow: Re > 3000.
Using the equation for the Reynolds number in the previous slide and cross sectional area of the pipe, we can obtain the volumetric flow rate corresponding to these regimes.

## Slide 16
We can rearrange the equation for Re to find the volumetric flow rates corresponding to each flow regimes.
and
Number of Runs
Notes: Use the equation michael disccussed for RE, By rearranging the equation for re and substituting the values at the flow regime limits, we can calculate the the flow rate where flow will change

## Slide 17: Flow Rate Increments
We want to do 7-10 runs in each flow regime, considering the time limitation for the experiment.
Flow Regime | Laminar | Transition | Turbulent
Flow rate range (L/hr) | 0<Q<63 | 63<Q<95 | Q>95
Flow Rate increment (L/hr) | 6 | 4 | 150
Notes: Substituting in Re=2000 and Re=3000 as the flow regime limits, we find the flow rates where flow will transition, and can then calculate by how much to increment flow rate between measurements
To do 7-10 runs in each regime, we must increment the flow by:

## Slide 18
Starting Flow rate
Start with low flowrate to see the clear transition from laminar to turbulent flow with the dye.
Start with lowest range gauges, then switch over as flow rate increases
Notes: We have decided to Start with low flowrate to see the clear transition from laminar to turbulent flow with the dye.
We will use gauge and rotameter with lower limit at the start of the lab to obtain the most accurate result. And then switch gauges as we increase the flow rate, this helps avoid damaging the gauges
Starting with high flow rate results higher pressure drop along the pipe which might damage the equipment e.g. over exceeding capacity of pressure gauges.

## Slide 19: Pressure Gauge To Use
Use the Moody diagram to find the theoretical corresponding to different flow rates used.
Use the Mechanical Energy Balance to find the corresponding theoretical pressure drop.
The pressure gauge which has the correct range will give the highest accuracy.

## Slide 20: Pressure Gauge To Use
Can calculate Re for any given flow rate
Can then find from Moody diagram
Notes: Native dynamics estimates glass pipe to have an absolute roughness of 0.0015mm
Pipe has diameter 12.6mm

## Slide 21: Pressure Gauge To Use
Rearranging the MEB, we get
Flow Rate (L/hr) | Estimated ∆P (pa) | Pressure gauge to use
<130 | <250 | Capsuhelic differential
130-1200 | 250<∆P<10,000 | Inverted water-air
>1200 | >10,000 | Wet-wet digital

## Slide 22: Pressure Gauges
Apparatus Connection

## Slide 23: Connecting Pressure Gauge
Capsuhelic differential pressure gauge- connect the brass connection fittings to the back port of the gauge and then connect the tubes to the two ends of the pipe to measure the pressure difference. It is also important to make sure seal tape is used while screwing the brass connection to prevent any air leaks that might affect the pressure result.

## Slide 24: Connecting Pressure Gauge
Inverted water-air manometer- connect the tube to the two ends of glass pipe. Due to the different amount of force applied to the fluid, the amount of fluid been pushed up into the manometer from the two ends are different and pressure differences can be calculated.
Wet-wet digital manometer- Connect the tubing to the two ends of the pipe and read the pressure difference.
Leave Gaps

## Slide 25: Flow Meters
Apparatus Connection

## Slide 26: Connecting Flow Meter
The flow meters will be connected at the start of the piping, just after the flowrate adjustment components.
Because of the way rotameters work, they must be connected vertically and in-line with the piping for accurate readings
The connection of flow meter will cause pressure difference (when flow increase, more pressure drops occurs) therefore it needs to be attached at the start of the piping to get accurate measures.

## Slide 27: References

## Slide 28: References
“Absolute roughness of pipe material” Neutrium, Native Dynamics, 19 May 2012, neutrium.net/fluid-flow/absolute-roughness-of-pipe-material/.
https://www.youtube.com/watch?v=kIjMzpzQ6wo&t=104s
Ahmari, H. and Kabir, S., 2020. Experiment #4: Energy Loss In Pipes. [online] Uta.pressbooks.pub. Available at: <https://uta.pressbooks.pub/appliedfluidmechanics/chapter/experiment-4/> [Accessed 24 August 2020].

## Slide 29: References
Warwick.ac.uk. 2020. [online] Available at: <https://warwick.ac.uk/fac/sci/eng/staff/ymc/teaching/zhigang/handout.pdf> [Accessed 24 August 2020].
Kau.edu.sa. 2020. [online] Available at: <https://www.kau.edu.sa/Files/0057863/Subjects/Chapter%208.pdf> [Accessed 24 August 2020].

## Slide 30: Thank you!
Any questions?